## Slide 1: Microcontroladores
M.C. Gabriel Casarrubias Guerrero

## Slide 2: Descripción del microcontrolador
High-Performance RISC CPU:
Solo 49 instrucciones
Todas se ejecutan en un ciclo de instrucción excepto los saltos a funciones.
Velocidad de operación:
Entrada de reloj/Oscilador hasta 32 MHz
Ciclo de instrucción de 125 ns
Capacidad de interrupción con contexto de guardado automático.
16 Niveles de profundidad del stack con reset por overflow/underflow
Modos de direccionamiento directo, indirecto y relativo.

## Slide 3: 2.1 Componentes del microcontrolador
Oscilador interno de precisión de 32MHz a 31KHz seleccionable
Modo sleep ahorrador de energía.
Power on reset (POR)
Power up timer (PWRT)
Timer de puesta en marcha del oscilador (OST)
Brown out reset (BOR)
Master clear
Protección de código programable
Célula de alta resistencia Flash/Data EEPROM
  100,000 escrituras Flash
  1,000,000 escrituras data EEPROM
  Retención mayor de 40 años

## Slide 4: Bloques del microcontrolador
MEMORIA DEL PROGRAMA
MEMORIA DE DATOS
Oscilador
No volátil
(Flash)
Volátil
(SRAM)
Contiene las instrucciones del programa que le dicen al CPU que hacer
Contiene los datos para el control de las instrucciones
El cerebro
Ejecuta todas las
instrucciones,
lógica y procesamiento
matemático
CPU
Working
STATUS
OPTION
ALU
PIC16 Núcleo
Notes: 4
The CPU is the brains of the operation. Here all instruction, logic and mathematical operations are processed.
Next, the oscillator. This will act as the engine for the microcontroller. A car can have a lot of features but they don’t do you much good if there is no engine.
Program Memory is used to hold the instruction that will tell the CPU how to think. This is the code that you have written to define the application at hand.
Data Memory will store data under the control of the instruction for use by the CPU.
Important to note is that Program Memory is non-volatile. This means that even if you were to remove power and physically take the microcontroller out of the circuit, the code that you have programmed onto it will still exist the next time this device is powered up.
Data Memory on the other hand is volatile. Removing power from the microcontroller will erase any values that were stored here.
Also note there is a lot more Program Memory on chip than Data Memory (hence the reason for the large PM block).

## Slide 5: Bloques del microcontrolador
Memoria del programa
Oscilador
CPU
Working
STATUS
OPTION
ALU
MEMORIA DE DATOS
TIMERS
10 BIT ADC
EEPROM
Cap/ Com/ PWM
SPI / I2C
USART
COMPARATORS
VOLTAGE REF
I/O PORTS
Peripherals Hang Off the Data Bus
PIC16 Núcleo
Notes: 5
Notice the size of the Program Memory and Data Memory areas on this slide. They have been drawn to scale (PIC16F877A: PM = 8Kx14, DM=368x8) to show the relative size of these areas in terms of # of bits. Note that there is a lot more Program Memory on chip than Data Memory.
All peripherals are connected to the Data Memory bus.

## Slide 6: MEMORIA DE PROGRAMA FLASH
Guarda las instrucciones (tu código)
  Le dice al CPU que hacer
Dividida en páginas de 2K x 14 bit
La cantidad de memoria depende del dispositivo específico
  56 K x 14 max (32 pages)
Todas las instrucciones son de 14 bits de longitud
  1 instrucción = 1 Dirección de la memoria del programa
MEMORIA DEL PROGRAMA
14-BITS LONGITUD
Página 1
Página 0
Página 2
Página 3
Notes: 6

## Slide 7: Memoria Flash del Programa ¿Por qué necesitamos paginar la memoria del programa?
Con instrucciones de 14 bits, solo once pueden usarse para especificar la Dirección de memoria en un solo ciclo.
MEMORIA DEL PROGRAMA
Page 1
Page 0
Page 2
Page 3
211 = 2048 direcciones
0
1
2
3
4
5
6
7
8
9
10
11
Opcode
GOTO Instruction in Program Memory
12
13
0000h
07FFh
0800h
0FFFh
1000h
17FFh
1800h
1FFFh
Notes: 7

## Slide 8: Memoria de datos SRAM
Dividida en bancos de 128 x 8 bit
La cantidad de memoria de datos depende del dispositivo
  4K x 8 max (63 banks) for the Enhanced Mid-Range core
2 grupos de registros:
  Special Function Registers (SFR)
    Controlar CPU y funciones de los periféricos
  General Purpose Registers (GPR)
    Guarda las variables definidas por el usuario
MEMORIA DE DATOS
SFR
GPR
8-bits Longitud
Bank 0
Notes: 8
Data Memory on the Baseline PIC Microcontroller is made up of 8-bit registers. Each one of these 8-bit registers have their own specific address location. Data memory registers are grouped in blocks called BANKS.These 8-bit registers are collectively store in blocks called banks. There are two types of data memory: Special Function Registers and General Purpose registers.

## Slide 9: Bancos de la memoria de datos ¿Por qué necesitamos los bancos de la memoria?
Con instrucciones de 14 bits, solo 7 bits pueden ser usados para especificar la Dirección en un ciclo
27 = 128 addresses
0
1
2
3
4
5
6
7
8
9
10
11
Opcode
Byte Oriented Instruction (i.e. ADDWF)
12
13
Bank 0
000h
07Fh
SFR
GPR
MEMORIA DE DATOS
Notes: 9
Why are there less bits to decode a data memory address than a program memory address? There are 20 instructions that require a data memory address, so more bits are needed to decode these. There are only 2 instructions (GOTO, CALL) that require a program memory address, so we can devote more bits to decoding the address.
The STATUS register holds additional bits (RP0, RP1, IRP) that are used to select the data bank. These bits can be thought of as additional data memory address bits.

## Slide 10: Seleccionando el banco active de la memoria de datos.
bit 0
bit 7
Bank Select Register (BSR)
BSR4
BSR3
BSR2
BSR1
BSR0
Selecciona el banco antes de accede a los registros del mismo
00000 = Bank 0
00001 = Bank 1
00010 = Bank 2
…….
11111 = Bank 31
Notes: 10
The status register not only determines the current data memory bank, but is an excellent resource to get an overview of what is occurring at a given time in the MCU.
  As shown in the slide, a variety of situations can be observed by noting individual bit values denoting events such as ALU status, and RESET status.
  Banking is achieved by setting the RP1 and RP0 bits in bit positions 6 and 7. As mentioned previously, to change a specific register in data memory, it is important to ensure that the appropriate Bank has been selected. Otherwise, the register will not be modified and could lead to programming errors.
  The IRP bit is used for indirect addressing modes by concatenating with the 8th bit of the File Select Register (FSR). This register will behave much like a pointer by holding an address in memory. An offset could be added to the FSR effectively incrementing or decrementing the address.

## Slide 11: SFR memoria de datos Registros de función especial
INDF0
INDF1
PCL
STATUS
FSR0L
FSR0H
FSR1L
ADRESL
FSR1H
BSR
WREG
PCLATH
INTCON
PORTA
ADCNT
SSP1BUF
PORTB
ADRESH
ADRPT
SSP1ADD
Bank 0
Bank 1
Bank 2
000
001
002
003
004
005
006
007
008
009
00A
00B
00C
00D
080
081
082
083
084
085
086
087
088
089
08A
08B
08C
08D
100
101
102
103
104
105
106
107
108
109
10A
10B
10C
10D
180
181
182
183
184
185
186
187
188
189
18A
18B
18C
18D
Ver hoja de datos para cada dispositivo en específico
INDF0
INDF1
PCL
STATUS
FSR0L
FSR0H
FSR1L
FSR1H
BSR
WREG
PCLATH
INTCON
INDF0
INDF1
PCL
STATUS
FSR0L
FSR0H
FSR1L
FSR1H
BSR
WREG
PCLATH
INTCON
INDF0
INDF1
PCL
STATUS
FSR0L
FSR0H
FSR1L
FSR1H
BSR
WREG
PCLATH
INTCON
Notes: 11
This is a view of the low addresses of the four banks, showing the SFRs. Note that some SFRs are available in more than one bank. In particular, take note of the STATUS register, which contains the bits that determine which bank is active.

## Slide 12: Set de instrucciones PIC16
35 instrucciones de solo una palabra
Todas se ejecutan en un ciclo de instrucción excepto los saltos
Byte Oriented Operations
Bit Oriented Operations
addwf f,d
andwf f,d
clrf f
clrw -
comf f,d
decf f,d
decfsz f,d
incf f,d
incfsz f,d
iorwf f,d
movf f,d
movwf f
nop -
rlf f,d
rrf f,d
subwf f,d
swapf f,d
xorwf f,d
Add W and f
AND W with f
Clear f
Clear W
Complement f
Decrement f
Decrement f, Skip if 0
Increment f
Increment f, Skip if 0
Inclusive OR W with f
Move f
Move W to f
No Operation
Rotate Left f through Carry
Rotate Right f through Carry
Subtract W from f
Swap nibbles in f
Exclusive OR W with f
bcf f,b
bsf f,b
btfsc f,b
btfss f,b
Bit Clear f
Bit Set f
Bit Test f, Skip if Clear
Bit Test f, Skip if Set
Literal and Control Operations
addlw k
andlw k
call k
clrwdt -
goto k
iorlw k
movlw k
retfie -
retlw k
return -
sleep -
sublw k
xorlw k
Add literal and W
AND literal with W
Call subroutine
Clear Watchdog Timer
Go to address
Inclusive OR literal with W
Move literal to W
Return from interrupt
Return with literal in W
Return from Subroutine
Go into standby mode
Subtract W from literal
Exclusive OR literal with W
Notes: 12
Development is easy with only 35 instructions to learn
Any instruction that changes program flow (branches, subroutine calls, subroutine returns, and instructions that test and skip the next instruction) will take two cycles
Instructions are grouped into three categories: byte-oriented, bit-oriented, and literal and control operations

## Slide 13: Set de instrucciones PIC16
Byte Oriented Operations
addwfc f,d
asrf f,d
lslf f,d
lsrf f,d
subwfb f,d
Add with Carry W and f
Arithmetic Right Shift
Logical Left Shift
Logical Right Shift
Subtract with Borrow W from f
Literal and Control Operations
movlp k
movlp k
bra k
brw -
callw -
addfsr n,k k
moviw n,mm
movwi n,mm
reset -
Move Literal to PCLATH
Move Literal to BSR
Branch Relative (signed)
Branch PC + W (unsigned)
Call PCLATH:W
Add Literal to FSRn (signed)
Move Indirect to W
Move W to Indirect
Reset Hardware & Software
Notes: 13
Development is easy with only 35 instructions to learn
Any instruction that changes program flow (branches, subroutine calls, subroutine returns, and instructions that test and skip the next instruction) will take two cycles
Instructions are grouped into three categories: byte-oriented, bit-oriented, and literal and control operations

## Slide 14: Guardado de contexto rápido
Interrupciones guardan automáticamente el contexto
  W
  STATUS
  BSR
  FSRs
  PCLATH
RETFIE automáticamente restaura el contexto
No se puede deshabilitar el fast context save
Notes: One extra complexity of all interrupt service routines is saving/restoring the context.
This is not difficult because you simply need to copy the code from the Microchip supplied template.
Unfortunately, it adds time to the ISR. To speed this process the PIC18 has a fast return option that allows an optional hardware context save.
The new PIC16 has a hardware context save but it is not optional.
The existing save/restore code can simply be removed. If your application does something unusual with the context after an interrupt that code will need to be rewritten to use the context save registers that are located in bank 31. The save registers are made available so the debugger can show them but this is also useful for operating systems and user creativity.
The RETFIE instruction now restores the context in addition to setting the GIE. Be careful because some legacy code uses the RETFIE at the end of the initialization code to save one instruction (BSF INTCON,GIE)
<CLICK MOUSE>