## Slide 1: Microcontroladores
M.C. Gabriel Casarrubias Guerrero

## Slide 2: 1.5.5 Distribución de terminales
Alimentación

## Slide 3: Puertos I/O

## Slide 4: ¿Qué son los bits de configuración?
Son usados para configurar las caracteristicas del nucleo:
  Code Protect
  Watchdog Timer
  Oscillator Options
  Debug Options
  More…
Vector de reset
Flash de usuario
Registros de configuración
Device ID
14-bit Program Memory
Registro CONFIG está localizado en la memoria del programa, fuera del rango del espacio del código de ejecución.
Memoria de usuario
Memoria de configuración
Vector de interrupción
Notes: 4
The configuration word, which is only accessible at programming time, is used to setup various options for the PICmicro, such as whether or not the Watchdog Timer should be enabled, what kind of oscillator will be used, and so on.

## Slide 5: Ejemplo de palabra de configuración
FCMEN
---
CSWEN
---
---
CLKOUTEN
---
RSTOCS2
RSTOCS1
RSTOSC0
---
FEXTOSC2
FEXTOSC1
FEXTOSC0
bit 0
bit 13
CONFIG1 (Osciladores)
DEBUG
STVREN
PPS1WAY
ZCDDIS
BORV
---
BOREN1
BOREN0
LPBOREN
---
---
---
PWRTE
MCLRE
bit 0
bit 13
CONFIG2 (Supervisores)
WTDCCS2
WTDCCS1
WTDCCS0
WTDCWS2
WTDCWS1
WTDCWS0
---
WDTE1
WDTE0
WDTCPS4
WDTCPS3
WDTCPS2
WDTCPS1
WDTCPS0
bit 0
bit 13
CONFIG3 (Windowed WatchDog)
LVP
SCANE
---
---
---
---
---
---
---
---
---
---
WRT1
WRT0
bit 0
bit 13
CONFIG4 (Memory)
---
---
---
---
---
---
---
---
---
---
---
---
CPD
CP
bit 0
bit 13
CONFIG5 (Code protection)
Notes: 5
The configuration word, which is only accessible at programming time, is used to setup various options for the PICmicro, such as whether or not the Watchdog Timer should be enabled, what kind of oscillator will be used, and so on.

## Slide 6: Características del reloj del sistema
XT
HS
LP
RC
INTRC
Cristal oscilador frecuencia estándar
Cristal oscilador de alta frecuencia
Cristal oscilador de baja frecuencia
Oscilador RC externo
Oscilador RC interno
100kHz - 4MHz
4MHz - 20MHz
5kHz - 200kHz
DC - 4MHz
4 o 8 MHz  2%
Opciones seleccionables del reloj proveen gran flexibilidad al diseñador:
  LP Oscilador diseñado para el menor consumo de corriente
  RC o INTRC provee una solución de ultra bajo costo de oscilador.
  XT optimizado para las frecuencias de oscilador mas comúnmente usadas
  HS optimizada para manejar cristales o resonadores de alta frecuencia

## Slide 8: OSCILATOR CONTROL REGISTERS
---
NOSC2
NOSC1
NOSC0
NDIV3
NDIV2
NDIV1
NDIV0
Registro OSCCON1
Bit 0
Bit 7
U-0
R/W
R/W
R/W
R/W
R/W
R/W
R/W
NOSC<2:0> COSC<2:0> | Clock source
111 | EXTOSC
110 | HFINTOSC
101 | LFINTOSC
100 | SOSC
011 | Reserved
010 | EXTOSC with PLLx4
001 | HFINTOSC with PLLx2
000 | Reserved
NCDIV<3:0> CDIV<3:0> | Clock divider
1111-1010 | Reserved
1001 | 512
1000 | 256
0111 | 128
0110 | 64
0101 | 32
0100 | 16
0011 | 8
0010 | 4
0001 | 2
0000 | 1

## Slide 9: 1.5.6 El reset y sus posibles fuentes
Power-On Reset (POR)
Brown-out Reset (BOR)
MCLR Reset
WDT reset
Instrucción RESET
Stack overflow
Stack underflow
Programming mode exit

## Slide 10: Windowed Watchdog Timer
Ayuda a recuperación de un mal funcionamiento de software
Usa su propio oscilador RC on-chip
WDT es limpiado por la instrucción CLRWDT
Una vez habilitado el WDT no puede ser deshabilitado por software
El desbordamiento del WDT resetea el chip
Periodo de tiempo programable:1ms a 250s
Opera en modo Sleep; cuando se cumple el tiempo, despierta el CPU
Tamaño de la ventana configurable de12.5 a 100 porciento de el periodo programado
Notes: 10
The primary purpose of the watchdog timer is to help the microcontroller recover from a software malfunction such as an infinite loop. As such, it cannot be disabled in software. Once it is enabled in the configuration word we saw earlier, it will be on forever and the only thing you can do is clear it via the CLRWDT instruction.
One very unique aspect of our WDT is that it runs from its own internal RC oscillator and is not dependent in any way on the system oscillator. Because the crystal is one of the most fragile components of the system, it can easily be shattered or disconnected, leaving the microcontroller without a clock source. Since the WDT runs independently, it can continue to run in the absence of a system clock and still reset the device into a known state. If your hardware is designed properly, you can take advantage of this fact to add some degree of hardware protection to your system.

## Slide 11: Generación del reset interno
POR: Power On Reset
  Con MCLR conectado a VDD, un pulso de reset es generado cuando se detecta una subida en VDD
PWRT: Power Up Timer
  64 ms (nominal)
  Desacoplado del BOR
OST: Oscillator Startup Timer
  Mantiene en reset el dispositivo por 1024 ciclos
  Permite que se estabilice el cristal o resonador.
VDD
MCLR
On Chip Reset Circuit
Internal Reset
Internal Reset
VDD
MCLR
POR
PWRT
OST
TPWRT
TOST
Reset
Execution
Notes: 11
The PICmicro offers a number of features that allow you to eliminate external circuitry that has traditionally been required with other microcontrollers.
Power on reset (POR) feature allows you to tie the MCLR (master clear) line to VDD without any additional components except perhaps a current limiting resistor. The necessary reset pulse will be automatically generated when a rise in Vdd is detected.
The Power Up Timer (PWRT) is used to prevent the PICmicro from starting up in an unstable state before the power supply has had a chance to ramp up and settle. The PWRT will hold the PICmicro in reset for about 72ms to ensure that in all but the most extreme cases, that the power supply has stabilized before the microcontroller is allowed to begin executing code.
The oscillator startup timer (OST) is automatically enabled for any oscillator mode except the RC modes. Its job is to ensure that the oscillator has enough time to stabilize in both amplitude and frequency before code begins executing to avoid any unpredictable behavior that can result from starting up with unstable conditions. The timer will hold the device in reset for 1024 cycles of whatever frequency the oscillator is running at.

## Slide 12: Brown Out Reset (BOR)
Cuando el voltaje cae por debajo de un nivel particular, el dispositivo entra en reset
Previene una operación errónea o inesperada
Elimina la necesidad de un circuito externo de BOR
Notes: 12
There are two types of brown out protection available for the PICmicro, a standard fixed brown out that is triggered at around 4V, and a programmable brown out with several available trip points.
The brown out circuit monitors the supply voltage and if it drops below the threshold, the PICmicro is immediately put into reset mode to prevent erratic behavior where the voltage might be below the minimum Vdd parameter.
(Functional description on graphic slide 46)

## Slide 13: Reset Brown Out Programable (PBOR)
Opciones de configuration(se ajustan al tiempo de programar)
  No se puede habilitar / deshabilitar por software
Dos BVDD puntos programables:
  1.9V
  1.8V
Notes: 13
The programmable BOR provides additional flexibility with 4 selectable trip points.

## Slide 14: BOR Operation
Mantiene al MCU en reset hasta ~64ms despues de detectar el nivel adecuado en VDD
Notes: 14
The brown out basically puts the part into reset whenever Vdd drops below the brown out threshold.
When the brown out condition ends, an internal RC timer starts and continues to hold the device in reset for 72ms before letting it run again. If another brown out occurs while the timer is counting, it will be reset.
The brown out module will hold the device in reset for as long as it takes as long as the voltage is high enough to keep it running.

## Slide 15: Modo Sleep
Eventos que despiertan al procesador del modo sleep
MCLR
WDT
INT
TMR1
ADC
CMP
CCP
PORTB
SSP
El procesador puede ser puesto en un modo de bajo consume ejecutando la instrucción sleep
  El Sistema del oscilador es parado
  EL estatus del procesaor es mantenido
  Watchdog timer sigue corriendo, si está habilitado
  Corriente minima consumida (0.1 - 2.0A)
Master Clear Pin pulso bajo
Watchdog Timer Timeout
Interrupción pin INT
Interrupción Timer 1
Interrupción de conversion A/D completa
Interrupción por cambio en la salida del comparador
Evento de captura de entrada
Interrupción por cambio eb el PORTB
Synchronous Serial Port (I2C Mode) Start / Stop Bit Detect Interrupt
Notes: 15
In today’s world of battery powered applications, low power modes are more critical than ever. All PICmicro devices provide a sleep mode in which the system oscillator is completely stopped, along with all peripherals dependent on that oscillator, such that the system is drawing little more than leakage current in the 0.1 to 2 microamp range.

## Slide 16: Tarea
3.4 Características de la fuente de alimentación y consumo de corriente del microcontrolador

## Slide 17: Funcionamiento básico
5v
0.1uF

## Slide 18: Funcionamiento básico
5v
0.1uF

## Slide 19: Funcionamiento básico (programación)
5v
0.1uF

## Slide 20: ICSP In-Circuit Serial Programming